## Slide 2: Distance Vector Routing
Initial state - each node only knows distance to its neighbours.
Final state – each node knows distance to all other nodes and the next hop.
Each node maintains a table consisting of
  destination,
  cost distance to destination,
  next hop to the destination
A
B
C
E
D
1
5
3
9
4
2
Dest | Dist. | Next hop
A | 1 | A
C | 3 | C
E | 9 | E
Initial table of node B

## Slide 3: Procedure
Every node exchanges its routing information (distance, cost) with all its neighbours. Information about next hop is not shared.
Every router takes the following action upon receiving information from other routers.
  dx(y) = minv{c(x,v) + dv(y)}
dx(y) – least cost path from node x to y
minv – minimum value considered among all v neighbours of x

## Slide 4: Routing process
A
B
C
E
D
1
5
3
9
4
2
Dest | Dist. | Next hop
A | 5 | A
B | 3 | B
D | 4 | D
C’s initial routing table
Dest | Dist.
A | 0
B | 1
C | 5
Routing info received from A
Dest | Dist. | Next hop
A | 5 | A
B | 3 | B
D | 4 | D
C’s updated table
Distance to A = 5

## Slide 5: Routing process
A
B
C
E
D
1
5
3
9
4
2
C’s initial routing table
Dest | Dist.
A | 1
B | 0
C | 3
E | 9
Routing info received from B
Dest | Dist. | Next hop
A | 4 | B
B | 3 | B
D | 4 | D
E | 12 | B
C’s updated table
Distance to B = 3
Dest | Dist. | Next hop
A | 5 | A
B | 3 | B
D | 4 | D

## Slide 6: Routing process
A
B
C
E
D
1
5
3
9
4
2
C’s initial routing table
Dest | Dist.
C | 4
D | 0
E | 2
Routing info received from D
Dest | Dist. | Next hop
A | 4 | B
B | 3 | B
D | 4 | D
E | 6 | B
C’s updated table
Distance to D = 4
Dest | Dist. | Next hop
A | 5 | A
B | 3 | B
D | 4 | D

## Slide 7: When is information exchanged?
Link/node failure
Periodic updates